## Slide 1
GT Capstone Design
Dia-Bot Second Progress Report
Operation Omega
Andrew Galant (ME), Catherine Kasper (CmpE), Jason Piotter (ME),
Hunter Present (ME), Connor Truono (CmpE), & Douglas Walker (ME)

## Slide 2: Presentation Content
Problem Statement
Function Tree
Specifications
Design Methodology & Concepts
  Mechanical
  Electrical
  Features & User Interface
  Problem Alert Examples
  Software Architecture
Industrial Design
Societal Impact
Team Member Contributions
Stretch Goals & Future Work
Project Timeline

## Slide 3
Problem Statement
Design and build a diagnostic robot (”Dia-Bot”) to identify potential installation issues in Vanderlande’s shuttle and conveyor systems

## Slide 4: Function Tree

## Slide 5: Specifications
The following will be considered in the design:
Bot should be conveyable on traditional conveyor surfaces and traverse normal transitions
  Belts, rollers, curves, diverts
  Inclines, declines, merges, diverges
  In addition to being conveyed, this bot must also traverse those machines under its own power
Robust enough to withstand the vibration induced while navigating the system
Must fit within a 620mm x 400mm footprint within a height of 300mm
Maximum weight of 35kg allowed by conveyor systems
On board camera remotely controlled to provide 360° rotation and vertical tilting
Ability to track the bot’s position within the system to an accuracy of ± 12”
Track accelerative forces seen by a product through normal handling
Measure vibration and sound levels to help identify problems

## Slide 6: Design Concept: Mechanical Components
Concepts 1: Symmetric without Suspension
Selected Design
Analysis of Continuous Track vs. Wheels:
Concepts 2: Asymmetric with Suspension
Suspension Concept:
Concept 3: Symmetric with Suspension

## Slide 7: Chassis Assembly: Pulleys and Belt
Self-Tracking Belt: 1100mm Perimeter
50 Tooth Pulley: Drive Gear
30 Tooth Pulley: Idle Gear

## Slide 8: Chassis Assembly: Main Body and Suspension

## Slide 9: Modular Attachment Assembly

## Slide 10: Design Concept: Electrical
Raspberry Pi
Processing & System Controls
Wi-Fi module
On Dia-Bot
User Interface
Web Format
Data Outputs
Web Page
Note: Voltage calculations and suspension locked have not been finalized and will depend on part selection and design validation.
Rechargeable Battery
DC Voltage Converter
Source Voltage
Voltage
Accelerometer
vibration
Microphone
sound
Camera
environment
Voltage
LED
light
Voltage
Motor
Right Tread
Voltage
Motor
Left Tread
Voltage
Motor
Lowers bottom panel
Voltage
Servo
Locks Suspension
Voltage
Motor
Rotates Camera 360˚
Voltage
Motor
Tilts Camera Angle
Voltage

## Slide 11: Design Concept: Updated Electrical

## Slide 12: Design Concept: Electrical
Mandatory Criteria | Option 1 | Option 2 | Option 3
Location Positioning | GPS | On Dia-Bot algorithm with navigation and system map | Raw position data using telemetry
Movement Generation | DC Motors | AC Motors | Servo Motors
Processing Center | Arduino UNO Rev 3 | Raspberry Pi 4 | Mbed (LPC1768 Cortex-M3)
Power Source | Rechargeable: Lithium-ion battery | Rechargeable: Lead Acid or SLA Batteries | Non-rechargeable: Alkaline Cell Batteries (PP3)
Real Time Access to Dia-Bot Data | Wi-Fi | Bluetooth | Extra Long Wires
User Interface | Web Access through Computer or Tablet | Remote Control center with a fabricated push button interface | Virtual Reality Interface with Haptic Gloves
Electrical Components Evaluation

## Slide 13: Design Concept: Features & User Interface
Movement
  Speed and Direction
  Raise Treads + Suspension Lock
  Emergency Stop
Problem Alerts
  Preset and Custom Triggers
Camera Controls
  Direction
  Zoom
  Light
Live Data Streaming
  Camera Feed
  Sensors
Features
Notes: For initial design validation, off the shelf components and
Other problems and use cases will undoubtedly be discovered over time
  More specific features will be required
  Our goal is to give Vanderlande a functioning platform with the right tools to easily program future solutions

## Slide 14: Design Concept: User Interface (Alternate)
Camera Visuals
Speed
+
-
_
Controls
Direction
Forward
Backward
Right
Left
Stop
Lock
Angle
Photo
Left
Right
Up
Down
Light
On
Off
Zoom
+
-
 | Active | Threshold | Alerts
Vibration |  | m/s | 
Sound |  | dB | none
Throughput |  |  | none
Alerts
On
Off
On
Off
On
Off
XX
Error
Live Camera
Data Archive
_
Data
Motor Speed
XX m/s
Location (m, m, m)
(XX, YY, ZZ)

## Slide 15: Design Concept: User Interface (Data View)
Camera Visuals
Speed
+
-
_
X
Controls
Direction
Forward
Backward
Right
Left
Stop
Lock
Angle
Photo
Left
Right
Up
Down
Light
On
Off
Zoom
+
-
 | Active | Threshold | Alerts
Vibration |  | m/s | 
Sound |  | dB | none
Throughput |  |  | none
Alerts
On
Off
On
Off
On
Off
XX
Error
Data
Live Data & Data Archive
Sound Level (dB/s) | Motor Speed (m/s) | Temperature (˚F) | Position (m) | Vibration Levels
 | 00 When viewing data, the robot will automatically stop |  |  | 
X direction
Y direction
Z direction
Timestamp | Location
09/28/2021 10:30 AM | XX YY ZZ
09/28/2021 10:20 AM | XX YY ZZ
09/28/2021 10:10 AM | XX YY ZZ
Data Archive
Live Camera

## Slide 16: Problem Alert Examples
Excessive force
  Instantaneous accelerometer reading measures above a threshold
Excessive vibration
  Vibrational magnitude at certain frequencies above a threshold for a certain period of time
Specific vibrational or combinational pattern detected
  Ex. Resonant frequencies
Sound levels
  Excessive sound energy over a certain length of time

## Slide 17: Design Concept: Dia-Bot Movement
Forward-Left | Forward | Forward-Right
Left | Stop | Right
Backward-Left | Backward | Backward-Right

## Slide 18: Software Architecture: Multiprocessing
Main Process: GUI
TK Mainloop
Handles UI interactions and events
Visuals
Thread
Loop/5s:
Tells main thread to update display from visuals queue
Alerts
Thread
Loop/2s:
Tells main thread to check processing queue for alert trip values
GPIO Data Collection
Collection Thread
Loop @ sampling rate:
Reads sensors for new data, places in data queue
Data Processing
Data Collection
Loop/0.5s:
Reads all new data from the data queue
Create Visuals
Thread
Loop/3s:
Creates new data plot or other visual and adds to visuals queue
Processing
Thread
Loop/2s:
Processes incoming data to collect alert-relevant metrics, sends to processing queue
Thread Handler
(1)Starts child threads. (2)Loop/3s: check for shutdown message
(3)Closes and joins worker threads
Repeated for each data type

## Slide 19: Industrial Design

## Slide 20: Societal, Environmental, and Sustainability
Goal and Scope of Social Impact Assessment
Inventory Analysis Section Summary of Social Impact Assessment
Notes: Notes:
Will not remove jobs, but augment operators’ decision making
Batteries: using Vanderlande’s supply of Milwaukee 18V

## Slide 21: Team Member Contributions
Andrew: Prior Art Research, Attachment Design for Modular System
Grace: Team Organizer, UI Design, Electrical Block Diagram, Embedded Connections
Jason: Motor Research for required Torque and RPM, Social Impact Analysis
Hunter: Chassis Design with Custom and Stock Parts, Building Chassis in CAD, ID
Connor: Created Software and User Interface, Embedded Connection, Narrowed Project Scope, Editing
Douglas: Design Concept Ideation- Function Tree/Morph Chart, Main Body Design

## Slide 22: Project Timeline
Today
Thanksgiving Break
Week
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Report #1
Poster Draft
Final Poster & Video
Capstone Expo
Update
Update
Update
Update
Update
Update
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Vanderlande Meetings
Prototyping
Expo
Engineering Feasibility Updates
Reports
Key
Bids
Project Intro
Ideation
User needs, specs, standards & codes
Feedback
Register for Expo
Proposal
Report #2
Design Simulation
Design Evaluation
Gather Materials
Build Enclosure
Build Movement Mech.
Build Power Subsystem
Build User Interface
Build Electrical Subsystems
Final Report & Fab Package
Validate Prototype
Notes: Vanderlande Meetings have been set up as weekly meetings, but if there is ever a need to extend or cancel a meeting, we will reach out to them 1 business day in advance and email them with our progress updates.

## Slide 23: Appendix
Prototyping Progress

## Slide 24: User Interface

## Slide 25: UI + Motor Interaction

## Slide 26: Previous Function Tree

## Slide 27: Design Concept: Morph Chart
Servo Motors

## Slide 28: Stretch Goals & Future Work
Additional verification features
  Semi or Fully autonomous driving and navigation
  Swarm functionality with direct communication between bots
  Computer vision integration for visual problem detection
  Train other machine learning models for additional patterns
Investigate equipping the Dia-Bot with the ability to automatically fix certain common issues
Use in an installed system*
  Device testing
    Detect real problems
  Collect position data
    Verify and improve simulations
*Depending on Vanderlande’s client timelines, we may not get to test the Dia-Bot on a full system this semester
Notes: Convert the following to bullet points:
As the full scope of detecting installation problems will not be realized in a semester project. Our goal is to give Vanderlande a functioning platform with the right tools to create future solutions.
This will be key to delivering a successful product, as more problems and use cases will undoubtedly be discovered over time.